Appendix A- Matlab Code

Code for Sensitive Dependence/ Lyapunov Exp. Approximation

ptype = '3';

a1=5;

b1=3;

a2=.1;

b2=2;

d1=.4;

d2=.01;

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

f= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-d2*X(3,:)];

y0=[.8,.17,9.8]';

tmax=10000;

s=ode45(f, [0,tmax], y0, odeset('abstol',1e-10));

s2=ode45(f, [0,tmax], y0+[0;0;1e-8], odeset('abstol',1e-10));

ts = 0:1:tmax;

F = deval(s, ts)';   % equally-spaced time data

F2 = deval(s2, ts)';   % equally-spaced time data

%ts = s.x; F = s.y';  % unequal spaced time data

figure; semilogy(ts, abs(F-F2), '+-'); xlabel('time');ylabel('log');

figure;

if ptype=='3'

plot3(F(:,1), F(:,2), F(:,3));

xlabel('x');ylabel('y');zlabel('z');

elseif ptype=='2'

subplot(3,1,1);

plot(ts,F(:,1));

xlabel('time');ylabel('x');

subplot(3,1,2);

plot(ts,F(:,2));

xlabel('time');ylabel('y');

subplot(3,1,3);

plot(ts,F(:,3));

xlabel('time');ylabel('z');

end

Code for Jacobean Matrix used in Calculation of Lyapunov Exponent

function [x, DFx] = three_tier_time1map(xo)

% evolve for 1 time unit, including the j

a1=5;

b1=3;

a2=.1;

b2=2;

d1=.4;

d2=.01;

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

F= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-d2*X(3,:)]; % vec flow field

df1= @(u) (a1*(1+b1*u)-b1*a1*u)/(1+b1*u)^2;

df2= @(u) (a2*(1+b2*u)-b2*a2*u)/(1+b2*u)^2;

Df = @(X) [1-2*X(1,:)-df1(X(1,:))*X(2,:), df1(X(1,:)), 0;...

X(2,:)*df1(X(1,:)), df1(X(1,:))-df2(X(2,:))*X(3,:)-d1, df2(X(2,:));...

0, X(3,:)*df2(X(2,:)), df2(X(2,:))-d2];

% DF at X

J0 = eye(3);   % initial Jac matrix

% 12-component ODE flow given by 3 components of solution and 9 components

% of the J matrix (J satisfies the ODE dJ/dt = Df.J)

G = @(t,z) [F(t,z(1:3,:)); Df(z(1:3,:))*z(4:6,:); Df(z(1:3,:))*z(7:9,:); ...

Df(z(1:3,:))*z(10:12,:) ];

[ts, xs]  = ode45(G, [0 .1], [xo; J0(:)]);    % numerically solve in t domain

x = reshape(xs(end,1:3), [3,1]);     % extract the answer at the final time t=1

J = xs(end,4:end);   % same for the J components

DFx = reshape(J,[3 3]);    % send J out as a 3x3 matrix.

Code To Calculate Lyapunov Exponent from Jacobean

% lyapunov exponents in a flow in R^3,

% Needs the function lorenz_time1map.m which returns the time-1 map

% barnett 11/19/07

% Modified by Ben Bier 11/30/09

a1=5;

b1=3;

a2=.1;

b2=2;

d1=.4;

d2=.01;

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

f= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-d2*X(3,:)];   % vec flow field

y0=[.8,.17,9.8]';                              % IC

[ts, Xs]  = ode45(f, [0 2000], y0);    % numerically solve in t domain

figure;plot3(Xs(:,1), Xs(:,2), Xs(:,3), '-'); axis vis3d; % show the attractor

% test three_tier_time1map

[x, J] = three_tier_time1map(y0);

% Measure Lyapunov exponents...

% ----- Re-orthogonalizing version, repeated averaging

M = 10;                              % how many averaging loops

N = 500;                                  % how many its per meas step

x = [y0];

h = zeros(3,1);                    % place to store averaged lyap exps

for m=1:M

J = eye(3);                   % Id is where Jacobean starts

for n=1:N

fprintf('n=%d: x=(%g,%g,%g)\n', n, x(1),x(2),x(3))

[x Jx] = three_tier_time1map(x);

J = Jx*J;                        % update Jacobean

[Q,R] = qr(J);                   % re-orthogonalize

J = Q*diag(diag(R));             % but keep them correct lengths

end

rN = abs(diag(R));                  % print out progress

h = h + log(rN)/N;

end

h = h/M                          % final answer

%final answer

%h =

% 0.0186

%-0.0407

%-0.0755

% you can see the middle lyap exp is v close to 0 - in fact all flows have

% a zero exponent.

Code for Plotting Original Function/Sens. Dependence

%PARAMTER VALUES

a1=5;

a2=.1;

b2=2;

d1=.4;

d2=.01;

%---------------

%Parameters Varied

b1=3;

tmax=5000;

%----------------

%Initial Conditions

y0=[.8,.17,9.8];

y0_2=[.8,.17,9.8+1e-8];

%------------------

%HOLLINGS TYPE-II FUNCTIONS

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

%--------------------------

%ODE SYSTEM

f= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-d2*X(3,:)];

%---------

%ODE Soln

[ts,F]=ode45(f,[0,tmax],y0);

[ts2,F2]=ode45(f,[0,tmax],y0_2);

%--------

% %3D Plot

% plot3(x(1,(5000:end)),x(2,(5000:end)),x(3,(5000:end)));

% xlabel('x');ylabel('y');zlabel('z');

% title('limit cycle at b1=2.3')

% %-------

%

%Z Plot

plot(ts,F(:,2));

xlabel('time');ylabel('y');

%-----

hold on;

%Z Plot F2

plot(ts2,F2(:,2),'r-');

xlabel('time');ylabel('y');

%-----

legend('y0','y0+(0,0,10e-9)');

Code to create Bifurcation Diagram

clear

%NOTES ON FILTER_SPAN

%50 works for b1=2.2:2.3

%55 works for b1=2.3:2.4

%75 works for b1=2.4:2.5

%100 works for b1=2.5:4

%150 works for b1=4:6.2

%MATRIX SIZE

%max number of peaks for t=10,000 on b=2.2:6.2 is 216, initialized matrix

%to 250 just in case untested intermediate value has more peaks

%T values for smooth(z) and z don't perfectly line up. Code takes local

%maxima for smooth(z), and then finds max value on a range from t-t_bounds

%to t+t_bounds of z.

t_bounds=10;

%----------------------------------------------------------------------

%Max time for ODE Solver

tmax=15000;

ts=0:tmax;

%-----------------------

%Max number of peaks to make sure vector size is sufficient

max_peaks=1000;

%---------------------------------------------------------

%Inputs for linspace for b1 loop

b1max=2.2;

b2max=3.2;

n=1001;

%-------------------------------

%Counter for b1 loop

j=1;

%-------------------

%ZMAX and BS initialization

zmax=zeros(n,max_peaks);

bs=zeros(n,max_peaks);

%--------------------------

%PARAMTER VALUES

a1=5;

a2=.1;

b2=2;

d1=.4;

d2=.01;

%---------------

for b1=linspace(b1max,b2max,n)

%ADJUSTS filter_span

if (b1<2.234)

filter_span=50;

elseif(b1>=2.234 && b1<2.3)

filter_span=53;

elseif(b1>=2.3 && b1<2.4)

filter_span=55;

elseif(b1>=2.4 && b1<2.494)

filter_span=75;

elseif(b1>=2.494 && b1<2.5)

filter_span=80;

elseif(b1>=2.5 && b1<2.805)

filter_span=90;

elseif(b1>=2.805 && b1<2.830)

filter_span=100;

elseif(b1>=2.830 && b1<2.4)

filter_span=110;

else

filter_span=150;

end;

%-------------------

%HOLLINGS TYPE-II FUNCTIONS

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

%--------------------------

%ODE SYSTEM

f= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-d2*X(3,:)];

%---------

%y0 randomization

r1=rand;

r2=rand;

r3=rand;

y0=[((r1*.8)+.1),((r2*.4)+.05),(7+(6*r3))];

%----------------

%ODE Calculation, Smooth, Derivatives

F=ode45(f, [0,tmax], y0);

xyz=deval(F,ts);

xyz(:,(1:7500))=[];

y=smooth(xyz(3,:),filter_span,'lowess');

dy=gradient(y);

d2y=gradient(dy);

%------------------------------------

%Find local maxima of smooth function

max_approx_i=find(abs(dy)<5e-4 & d2y<0);

max_approx_f=max_approx_i(10:numel(max_approx_i)-10);

%------------------------------------

%Initialize vector of local max(z)

max_z_row=zeros(1,numel(max_approx_f));

b_row=zeros(1,numel(max_approx_f))+b1;

%---------------------------------

%Finds local maxima of z

for i=1:numel(max_approx_f)

max_z_row(i)=max(xyz(3,max_approx_f(i)-t_bounds:max_approx_f(i)+t_bounds));

end;

%-----------------------

%Resize b_row and max_z_row so they can be added into big matrix

if (isempty(max_z_row)==0)

b_row(numel(b_row)+1:max_peaks)=b1;

max_z_row(numel(max_z_row)+1:max_peaks)=max_z_row(1,1);

else

b_row=bs(j-1,:);

max_z_row=zmax(j-1,:);

end;

%---------------------------------------------------------------

%Update matrices of b1, max z's for plotting

bs(j,:)=b_row;

zmax(j,:)=max_z_row;

%-------------------------------------------

%Counter

j=j+1;

%-------

%Displays b1 values as progress tracker

disp(b1);

%--------------------------------------

end;

Code for Zero Crossings Function

function [v,ist,df] = foodchainzcross(t,x);

% event function for test_poincare.m

v = x(3)-9; % event is x(2)=0 (ie when v is zero)

ist = 1;  % if true, terminate evolution when this event occurs

df = -1;   % increasing sense only

Code to Create Poincaé Section and Time-delay plots

% test Poincare surface of section via ODE solver. Barnett 11/23/09

% modified by Peter Hughes 12/1/09

% (uses zerocross.m as event function defining the intersection event)

clear

%PARAMTER VALUES

a1=5;

a2=.1;

b2=2;

d1=.4;

d2=.01;

%---------------

%Parameters Varied

b1=3;

%----------------

%HOLLINGS TYPE-II FUNCTIONS

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

%--------------------------

%ODE SYSTEM

f= @(t,y) [y(1,:)*(1-y(1,:))-y(2,:)*f1(y(1,:));...

y(2,:)*f1(y(1,:))-y(3,:)*f2(y(2,:))-d1*y(2,:);...

y(3,:)*f2(y(2,:))-d2*y(3,:)];

%---------

tmax = 10000;       % max time to wait until next intersection

yo = [.8,.17,9.8];     % initial condition

ns = 500;         % how many intersection (iterations of P map)

tp = nan*(1:ns); yp = nan*zeros(numel(yo),ns); yi = yo; % init arrays

figure;

for n=1:ns

s = ode45(f, [0 tmax], yo, odeset('Events',@foodchainzcross));

if isempty(s.xe), disp('no intersection found!');

else

tp(n) = s.xe(end); yo = s.ye(:,end); yp(:,n) = yo;

end;

end;

subplot(2,1,1);

plot(yp(1,:),yp(2,:),'+');

xlabel('x'); ylabel('y');

title('PoincarÈ Section at z=9,b1=3')

subplot(2,1,2);

plot(yp(1,(1:end-1)),yp(1,(2:end)),'+');

xlabel('x(n)');ylabel('x(n+1)');

title('PoincarÈ Map for b1=3');

Code for Lyapunov Number Approximation for Poincaré Map

X(1,:)=yp(1,1:end-1);       %Time delay data from PoincarÈ Map

X(2,:)=yp(1,2:end);

X=X';   %Transpose so sortrows can be used

X=sortrows(X);     %Sorts data so slope can be taken

p=polyfit(X(:,1),X(:,2),10);    %Polynomial Approx.

z=polyder(p);       %Derivative of polynomial

subplot(2,1,1);

plot(X(:,1),polyval(p,X(:,1)));

hold on;

plot(X(:,1),X(:,2),'rx');

title('PoincarÈ Map and 10^t^h degree polynomial approximation');

subplot(2,1,2);

plot(X(:,1),polyval(z,X(:,1)));

xlabel('x(n)');ylabel('x(n+1)');

title('First derivative of polynomial approximation');

L=mean(abs(polyval(z,X(:,1))));         %L Calculation

xlabel('x(n)');ylabel('dx(n+1)/dx(n)');

disp('L=');

disp(L);

h=log(L);                               %h calculation

disp('h=');

disp(h);

X=X';

Code for 4-tier Population Model

a1=5;

b1=3;

a2=.1;

b2=2;

d1=.4;

d2=.01;

a3=.05;

b3=4;

d3=.009;

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

f3= @(u) (a3*u)/(1+b3*u);

f= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-X(4,:)*f3(X(2,:))-d2*X(3,:);...

X(4,:)*f3(X(3,:))-d3*X(4,:)];

y0=[.8,.17,9.8,1];

[ts,F]=ode45(f, [0,1000], y0);

plot3(F(:,1), F(:,2), F(:,3));

xlabel('x');ylabel('y');zlabel('z');

subplot(4,1,1);

plot(ts,F(:,1));

xlabel('time');ylabel('x');

subplot(4,1,2);

plot(ts,F(:,2));

xlabel('time');ylabel('y');

subplot(4,1,3);

plot(ts,F(:,3));

xlabel('time');ylabel('z');

subplot(4,1,4);

plot(ts,F(:,4));

xlabel('time');ylabel('zz');

Code for 4-tier model Lyapunov Exponent Approximation

a1=5;

b1=3;

a2=.1;

b2=2;

d1=.4;

d2=.01;

a3=.05;

b3=4;

d3=.009;

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

f3= @(u) (a3*u)/(1+b3*u);

f= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-X(4,:)*f3(X(2,:))-d2*X(3,:);...

X(4,:)*f3(X(3,:))-d3*X(4,:)];

y0=[.8,.17,9.8,1]';

tmax=925;

s=ode45(f, [0,tmax], y0, odeset('abstol',1e-10));

s2=ode45(f, [0,tmax], y0+[0,0,0,1e-8]', odeset('abstol',1e-10));

ts = 0:1:tmax;

F = deval(s, ts)';   % equally-spaced time data

F2 = deval(s2, ts)';   % equally-spaced time data

%ts = s.x; F = s.y';  % unequal spaced time data

figure; semilogy(ts, abs(F-F2), '+');

%[ts,F]=ode45(f, [0,2000], y0);

%?plot4(F(:,1), F(:,2), F(:,3));

%xlabel('x');ylabel('y');zlabel('z');

xlabel('time');ylabel('log');

figure;

subplot(4,1,1);

plot(ts,F(:,1));

xlabel('time');ylabel('x');

subplot(4,1,2);

plot(ts,F(:,2));

xlabel('time');ylabel('y');

subplot(4,1,3);

plot(ts,F(:,3));

xlabel('time');ylabel('z');

subplot(4,1,4);

plot(ts,F(:,4));

xlabel('time');ylabel('D');

Code for Cyclic Population Model

a1=5;

b1=3;

a2=.1;

b2=2;

d1=.4;

d2=.01;

a3=.5;

b3=1.5;

e1=.75;

e2=.55;

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

f3= @(u) (a3*u)/(1+b3*u);

f= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:))+X(1,:)*f3(X(2,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-d2*X(3,:);...

e1*d1*X(2,:)+ e2*d2*X(3,:)-X(1,:)*f3(X(2,:))];

y0=[.8,.17,9.8,1]';

tmax=2000;

s=ode45(f, [0,tmax], y0, odeset('abstol',1e-10));

s2=ode45(f, [0,tmax], y0+[0,0,0,1e-8]', odeset('abstol',1e-10));

ts = 0:1:tmax;

F = deval(s, ts)';   % equally-spaced time data

F2 = deval(s2, ts)';   % equally-spaced time data

%ts = s.x; F = s.y';  % unequal spaced time data

figure; semilogy(ts, abs(F-F2), '+');

%[ts,F]=ode45(f, [0,2000], y0);

%?plot4(F(:,1), F(:,2), F(:,3));

%xlabel('x');ylabel('y');zlabel('z');

xlabel('time');ylabel('log');

figure;

subplot(4,1,1);

plot(ts,F(:,1));

xlabel('time');ylabel('x');

subplot(4,1,2);

plot(ts,F(:,2));

xlabel('time');ylabel('y');

subplot(4,1,3);

plot(ts,F(:,3));

xlabel('time');ylabel('z');

subplot(4,1,4);

plot(ts,F(:,4));

xlabel('time');ylabel('D');

Code for Closed Cyclic Model

a1=5;

b1=3;

a2=.1;

b2=2;

d1=.4;

d2=.01;

a3=.5;

b3=1.5;

e1=.75;

e2=.55;

f1= @(u) (a1*u)/(1+b1*u);

f2= @(u) (a2*u)/(1+b2*u);

f3= @(u) (a3*u)/(1+b3*u);

f= @(t,X) [X(1,:)*(1-X(1,:))-X(2,:)*f1(X(1,:))+X(1,:)*f3(X(2,:));...

X(2,:)*f1(X(1,:))-X(3,:)*f2(X(2,:))-d1*X(2,:);...

X(3,:)*f2(X(2,:))-d2*X(3,:);...

e1*d1*X(2,:)+ e2*d2*X(3,:)-X(1,:)*f3(X(2,:))];

y0=[.8,.17,9.8,1]';

tmax=2000;

s=ode45(f, [0,tmax], y0, odeset('abstol',1e-10));

s2=ode45(f, [0,tmax], y0+[0,0,0,1e-8]', odeset('abstol',1e-10));

ts = 0:1:tmax;

F = deval(s, ts)';   % equally-spaced time data

F2 = deval(s2, ts)';   % equally-spaced time data

%ts = s.x; F = s.y';  % unequal spaced time data

figure; semilogy(ts, abs(F-F2), '+');

%[ts,F]=ode45(f, [0,2000], y0);

%?plot4(F(:,1), F(:,2), F(:,3));

%xlabel('x');ylabel('y');zlabel('z');

xlabel('time');ylabel('log');

figure;

subplot(4,1,1);

plot(ts,F(:,1));

xlabel('time');ylabel('x');

subplot(4,1,2);

plot(ts,F(:,2));

xlabel('time');ylabel('y');

subplot(4,1,3);

plot(ts,F(:,3));

xlabel('time');ylabel('z');

subplot(4,1,4);

plot(ts,F(:,4));

xlabel('time');ylabel('D');